## Slide 1: CMPE 110: Computer Architecture
Week 1
Performance
[Adapted in part from Jose Renau, Mary Jane Irwin, Joe Devietti, Onur Mutlu, and others]
Jishen Zhao (http://users.soe.ucsc.edu/~jzhao/)

## Slide 2: Announcements
TA office hours (location: E2-480)
  Akash Sridhar: Monday, 5-6pm
  Ramesh K. Jayaraman: Tuesday 2-3pm
  Meeta Sinha: Thursday 11am-12pm
Discussion sessions (location: E2-194)
  Section 1: Wed 3:30 – 4pm: Ramesh Jayaraman
  Section 2: Thu 8:30 – 9:40am: Meeta Sinha
  Section 3: Fri 2 – 3:10p: Akash Sridhar

## Slide 3: Review: What is computer architecture?
“Technology”
Logic Gates
SRAM
DRAM
Circuit Techniques
Packaging
Magnetic Storage
Flash Memory
Applications/Domains
Desktop
Servers
Mobile Phones
Supercomputers
Game Consoles
Embedded
Goals
Function
Performance
Reliability
Cost/Manufacturability
Energy Efficiency
Time to Market
Plans

## Slide 4: Today: Performance
Metrics
  Latency and throughput
  Speedup
  Averaging
CPU Performance
Notes: Overview of today’s class:
Metrics, how measure CPU performance,

## Slide 5: Performance Metrics

## Slide 6: Performance: Latency vs. Throughput
Latency (execution time): time to finish a fixed task
Throughput (bandwidth): number of tasks per unit time
  Different: exploit parallelism for throughput, not latency
Choose definition of performance that matches your goals
  Scientific program? latency.
  Web server? throughput.
Notes: The two principle metrics
Lat vs throughput diff: think about when you drive on a high way:
Lat about how long the high way is of course also need to consider speed limit; but it’s all about your car running on the high way, a single car
Throughput about how many lanes there are: the more the lanes the more the cars the high way can accommodate in parallel, the higher the throughput, so throughput focuses on many tasks rather than a single one

## Slide 7: Examples
How to measure the performance of moving people for 10 miles round trip?
  Car: capacity = 5, speed = 60 miles/hour
  Bus: capacity = 60, speed = 20 miles/hour
  Latency: how long does ~ take to move one person for 20 miles?
  Throughput: how many people can ~ move per hour?
Notes: 1. The same problem, measured with different metrics, things will be different
2. Question: What is the fastest way ~ What do you think?
(assuming 1 Gbits/second)
Answer: Used FedEx overnight to deliver the drive. 10 TB in, say, 15 hours is 1,300 mbits/second of bandwidth (600 GB/hour)
Amazon (maybe)
- screensho

## Slide 8: Examples
Fastest way to send 10TB of data from US to UK?
FTP, SMB, Rsync / Robocopy, other?
Notes: 1. The same problem, measured with different metrics, things will be different
2. Question: What is the fastest way ~ What do you think?
(assuming 1 Gbits/second)
Answer: Used FedEx overnight to deliver the drive. 10 TB in, say, 15 hours is 1,300 mbits/second of bandwidth (600 GB/hour)
Amazon (maybe)
- screensho

## Slide 10: What we learned
Measuring performance
Latency & throughput

## Slide 11: Comparing Performance - Speedup
Speedup of A over B
  X = Latency(B)/Latency(A) (divide by the faster)
  X = Throughput(A)/Throughput(B) (divide by the slower)
A is X% faster than B if
  X = ((Latency(B)/Latency(A)) – 1) * 100
  X = ((Throughput(A)/Throughput(B)) – 1) * 100
  Latency(A) = Latency(B) / (1+(X/100))
  Throughput(A) = Throughput(B) * (1+(X/100))
Car/bus example
  Latency? Car is 3 times (and 200%) faster than bus
  Throughput? Bus is 4 times (and 300%) faster than car
Notes: If two programs, A and B. want to compare them. How calculate?
When vendors advertise about their machines

## Slide 12: Car/bus example
Latency: car = 20 min, bus = 60 min
Throughput: car = 15 PPH, bus = 60 PPH
Speedup?
Latency:
  Speedup of car over bus is 3
  Car is 200% faster than bus
Throughput:
  Speedup of bus over car is 4
  Bus is 300% faster than car
Notes: If two programs, A and B. want to compare them. How calculate?
When vendors advertise about their machines

## Slide 13: Comparing Performance - Speedup
Program A runs for 200 cycles
Program B runs for 350 cycles
Speedup of A over B?
- Speedup = 350/200 = 1.75
- As a percentage…
If program C is 50% faster than A, how many cycles does C run for?
  133 cycles
What is “cycle”?
Execution time * clock frequency i.e., second * Hz
Notes: Let’s look a detailed example about how we calculate speedup
Say talking about Lat
Here things get a bit more complex

## Slide 14: Note
Speedup of A over B
  X = Latency(B)/Latency(A)
  X = Throughput(A)/Throughput(B)
What if X < 1?
-- means A is slower than B

## Slide 15: Speedup and % Increase and Decrease
Program A runs for 200 cycles
Program B runs for 350 cycles
Percent increase and decrease are not the same.
  % increase of cycles: ((350 – 200)/200) * 100 = 75%
  % decrease of cycles: ((350 - 200)/350) * 100 = 42.3%
Notes: Let’s look a detailed example about how we calculate speedup
Say talking about Lat
Here things get a bit more complex

## Slide 16: What we learned
Comparing performance
Speedup
Performance metrics
Latency, throughput, speedup

## Slide 17: Averaging performance

## Slide 18: Mean (Average) Performance Numbers
Arithmetic: (1/N) * ∑P=1..N Latency(P)
  For units that are proportional to time (e.g., latency)
Harmonic: N / ∑P=1..N 1/Throughput(P)
  For units that are inversely proportional to time (e.g., throughput)
You can add latencies, but not throughputs
  Latency(P1+P2, A) = Latency(P1, A) + Latency(P2, A)
  Throughput(P1+P2, A) != Throughput(P1, A) + Throughput(P2, A)
Geometric: N√∏P=1..N Speedup(P)
  For unitless quantities (e.g., speedup ratios)
Notes: Statistics terms
When should we use which one?
Rule of sum: add sth together, the sum needs to have a physical meaning
45 miles/hour Don’t do it now…
We’ve seen how to average latency & throughput, how about speedup?

## Slide 19: For Example…
    1 mile @ 30 miles/hour + 1 mile @ 90 miles/hour
You drive two miles
  30 miles per hour for the first mile
  90 miles per hour for the second mile
Question: what was your average speed?
  Hint: the answer is not 60 miles per hour
  Why?

## Slide 20: Answer: 45 miles/hour
You drive two miles
  30 miles per hour for the first mile
  90miles per hour for the second mile
Question: what was your average speed?
  .03333 hours per mile for 1 miles
  .01111 hours per mile for 1 mile
  .04444 hours for 2 miles
  = 45 miles per hour
  Throughput = harmonic (inverse proportionate to time)
  Latency = arithmetic (proportionate to time)

## Slide 21: What we learned
Averaging performance
Arithmetic mean for latency
Harmonic mean for throughput
Geometric mean for speedup

## Slide 22: CPU Performance
How to evaluate
Latency, throughput, and speedup

## Slide 23: CPU Performance Equation
Latency = seconds / program =
  (insns / program) * (cycles / insn) * (seconds / cycle)
    NOTE: insns = instructions
  Insns / program: insn count
    Impacted by program, compiler, ISA
  Cycles / insn: CPI [Note: CPI big part of class]
    Impacted by program, compiler, ISA, micro-arch
  Seconds / cycle: clock period (Hz)
    Impacted by micro-arch, technology
For low latency (better performance) minimize all three
  Difficult: often pull against one another (there are tradeoffs, cannot achieve all three. In computer architecture you want to find a balance in all 3)
  Example we have seen: RISC vs. CISC ISAs
    RISC: low CPI/clock period, high insn count
    CISC: low insn count, high CPI/clock period
Notes: Have leaned in CMPE 110
Can be calculated in this way

## Slide 24: Cycles per Instruction (CPI)
CPI: Cycles/instruction (CPI is a concept of latency)
  IPC = 1/CPI (IPC is throughput)
    Used more frequently than CPI
    Favored because “bigger is better”, but harder to compute with
  Different instructions have different cycle costs
    E.g., “add” typically takes 1 cycle (easier) , “divide” takes >10 cycles
  Depends on relative instruction frequencies (what if idle)
CPI example
  A program executes equal: integer, floating point (FP), memory ops
  Cycles per instruction type: integer = 1, memory = 2, FP = 3
  What is the CPI? (1 cycle+2 cycles +3 cycles) / 3 instrs= 2
  Calculated in another way: 33% x 1 + 33% x 2 + 33% x 3 = 2
Notes: A bit more about CPI
Idle
Assign papers reading, not part of paper review assignment, just elevator pitch summary, discuss next week

## Slide 25: CPI Example
Assume a processor with instruction frequencies and costs
  Integer ALU: 50%, 1 cycle
  Load: 20%, 5 cycle
  Store: 10%, 1 cycle
  Branch: 20%, 2 cycle
Which change would improve performance more?
  A. “Branch prediction” to reduce branch cost to 1 cycle?
  B. Faster data memory to reduce load cost to 3 cycles?
Compute CPI
  Base = .5*1+.2*5+.1*1+.2*2 = 2 CPI
  A = .5*1+.2*5+.1*1+.2*1 = 1.8 CPI
  B = .5*1+.2*3+.1*1+.2*2 = 1.6 CPI -> B is better
Notes: - Design choice – emph set by program vs procesor

## Slide 26: Measuring CPI
How are CPI and execution-time actually measured?
  Execution time? stopwatch timer (Unix “time” command)
  Cycles = execution time * clock frequency
  How is instruction count measured?
Hardware event counters
  Available in most processors today
  One way to measure instruction count
Cycle-level micro-architecture simulation (no simulation in this class)
  Measure exactly what you want … and impact of potential fixes!
  Method of choice for many micro-architects
More useful is CPI breakdown (CPICPU, CPIMEM, etc.)
  So we know what performance problems are and what to fix
   truly executed insn
Notes: - Mention ghz

## Slide 27: What we learned
How to evaluate CPU performance
CPI
(IPC)

## Slide 28: Next class
Performance
ISA