## Slide 1: CMPE 110: Computer Architecture
Week 2
ISA
[Adapted in part from Jose Renau, Mary Jane Irwin, Joe Devietti, Onur Mutlu, and others]
Jishen Zhao (http://users.soe.ucsc.edu/~jzhao/)

## Slide 2: Review: Performance
Performance metrics: Latency & throughput
Comparing performance: Speedup
Averaging performance:
  Arithmetic mean
  Harmonic mean
  Geometric mean
Measuring CPU performance: CPI (IPC)
Amdahl’s Law
  How much does an optimization improve performance?
Benchmarks

## Slide 3: Today:
Instruction set architecture (ISA)
  What is ISA?
  Execution model
    Program execution model
    Instruction execution model
  ISA design goals

## Slide 4: Instruction Set Architecture (ISA)

## Slide 5: ISA Overview
What is an ISA?
  An ISA includes a specification of the set of opcodes (machine language), and the native commands implemented by a particular processor. <Wikipedia>
  A functional contract
All ISAs similar in high-level ways
  But many design choices in details
  Two “philosophies”: CISC/RISC
    Difference is blurring
Good ISA…
  Enables high-performance
  At least doesn’t get in the way
Application
OS
Firmware
Compiler
CPU
I/O
Memory
Digital Circuits
Gates & Transistors
ISA: Layer that helps each side talk to each other
- Ultimate goal: enable high performance
Notes: A complex instruction set computer (CISC) has many specialized instructions, some of which may only be rarely used in practical programs. A reduced instruction set computer (RISC) simplifies the processor by efficiently implementing only the instructions that are frequently used in programs, while the less common operations are implemented as subroutines, having their resulting additional processor execution time offset by infrequent use.

## Slide 6: Execution Model

## Slide 7: Program Compilation
Program written in a “high-level” programming language
  C, C++, Java, C#
  Hierarchical, structured control: loops, functions, conditionals
  Hierarchical, structured data: scalars, arrays, pointers, structures
Compiler: translates program to assembly
  Parsing and straight-forward translation
  Compiler also optimizes
  Compiler is itself a program…who compiled the compiler
  - Compiler (a program) translates programming language to assembly language
CPU
Mem
I/O
System software
App
App
App
int array[100], sum;
void array_sum() {
for (int i=0; i<100;i++) {
sum += array[i];
}
}
Notes: compiler often translates all the way to machine code

## Slide 8: Assembly & Machine Language
Assembly language
  Human-readable representation
Machine language
  Machine-readable representation
  1s and 0s (often displayed in “hex”)
Assembler
  Translates assembly to machine
CPU
Mem
I/O
System software
App
App
App
x9A00 CONST R5, #0
x9200 CONST R1, array
xD320 HICONST R1, array
x9464 CONST R2, sum
xD520 HICONST R2, sum
x6640 LDR R3, R1, #0
x6880 LDR R4, R2, #0
x18C4 ADD R4, R3, R4
x7880 STR R4, R2, #0
x1261 ADD R1, R1, #1
x1BA1 ADD R5, R5, #1
x2B64 CMPI R5, #100
x03F8 BRn array_sum_loop
Machine code
Assembly code

## Slide 9: Example Assembly Language & ISA
ARM: example of real ISA
  32/64-bit operations
  32-bit insns
  63 registers
    31 integer, 32 floating point
  ~100 different insns
CPU
Mem
I/O
System software
App
App
App
  cmp r1, #0
  push {r4}
  ble .L4
  movs r3, #0
  subs r2, r0, #4
  mov r0, r3
  .L3:
  adds r3, r3, #1
  ldr r4, [r2, #4]!
  cmp r3, r1
  add r0, r0, r4
  bne .L3
  .L2:
  pop {r4}
  bx lr
  .L4:
  movs r0, #0
  b .L2
Example code is ARM, but
all ISAs are pretty similar
Notes: Q: which is the destination register? R0

## Slide 10: Instruction Execution Model
A computer is just a finite state machine
  Registers (few of them, but fast)
    Temporary, where input/outputs stay, easier for machine to access
    Faster than disk
  Memory (lots of memory, but slower)
    Faster than disk but slower than registers
  Program counter (next insn to execute)
    Called “instruction pointer” in x86
    Stores pointers of addresses of instructions
A computer executes instructions
  Fetches next instruction from memory
  Decodes it (figure out what it does)
  Reads its inputs (registers & memory)
  Executes it (adds, multiply, etc.)
  Write its outputs (registers & memory)
  Next insn (adjust the program counter)
Program is just “data in memory”
  Makes computers programmable (“universal”)
CPU
Mem
I/O
System software
App
App
App
Fetch
Decode
Read Inputs
Execute
Write Output
Next Insn
Instruction  Insn

## Slide 11: What is an ISA? -- In more detail

## Slide 12: What Is An ISA?
ISA (instruction set architecture)
  A well-defined hardware/software interface
  The “contract” between software and hardware
    Functional definition of storage locations & operations
      Storage locations: registers, memory
      Operations: add, multiply, branch, load, store, etc
    Precise description of how to invoke & access them
Not in the contract: non-functional aspects (Quiz)
  How operations are implemented
  Which operations are fast and which are slow and when
  Which operations take more power and which take less
Instructions (Insns)
  Bit-patterns hardware interprets as commands

## Slide 13: ARM ADD Documentation
Notes: Too small, read out

## Slide 14: A Language Analogy for ISAs
Communication
  Person-to-person  software-to-hardware
Similar structure
  Narrative  program
  Sentence  insn
  Verb  operation (add, multiply, load, branch)
  Noun  data item (immediate, register value, memory value)
  Adjective  addressing mode
Many different languages, many different ISAs
  Similar basic structure, details differ (sometimes greatly)
Key differences between languages and ISAs
  Languages evolve organically, many ambiguities, inconsistencies
  ISAs are explicitly engineered and extended, unambiguous
  adds r3, r3, #1

## Slide 15: The Sequential Model
Basic structure of all modern ISAs
  Often called Von Neumann, but in ENIAC before
Program order: total order on dynamic insns
  Order and named storage define computation
  Order the program gets executed
Convenient feature: program counter (PC)
  Insn itself stored in memory at location pointed to by PC
  Next PC is next insn unless insn says otherwise
  Special register that stores location of next instruction
Processor logically executes loop at left
Atomic: insn finishes before next insn starts
  Implementations can break this constraint physically
  But must maintain illusion to preserve correctness
  The next instruction cannot get in the way, so one inst is executed atomically
Fetch
Decode
Read Inputs
Execute
Write Output
Next Insn

## Slide 16: ISA Design Goals

## Slide 17: What Makes a Good ISA?
Three Design Goals
Programmability (1)
  Easy to express programs efficiently?
Performance/Implementability (2)
  Easy to design high-performance implementations?
  Easy to design low-power implementations?
  Easy to design low-cost implementations?
Compatibility (3)
  Easy to maintain as languages, programs, and technology evolve?
  x86 (IA32) generations: 8086, 286, 386, 486, Pentium, PentiumII, PentiumIII, Pentium4, Core2, Core i7, …

## Slide 18: Programmability
Easy to express programs efficiently?
  For whom?
Before 1980s: human
  Compilers were terrible, most code was hand-assembled
  Want high-level coarse-grain instructions
    As similar to high-level language as possible
After 1980s: compiler
  Optimizing compilers generate much better code that you or I
  Want low-level fine-grain instructions
    Compiler can’t tell if two high-level idioms match exactly or not
This shift changed what is considered a “good” ISA…

## Slide 19: Implementability
Every ISA can be implemented
  Not every ISA can be implemented efficiently
Classic high-performance implementation techniques
  Pipelining, parallel execution, out-of-order execution (more later)
Certain ISA features make these difficult
  Variable instruction lengths/formats: complicate decoding
  Special-purpose registers: complicate compiler optimizations
  Difficult to interrupt instructions: complicate many things

## Slide 20: What Makes a Good ISA?
Programmability
  Easy to express programs efficiently?
Performance/Implementability
  Easy to design high-performance implementations?
  Easy to design low-power implementations?
  Easy to design low-cost implementations?
Compatibility
  Easy to maintain as languages, programs, and technology evolve?
  x86 (IA32) generations: 8086, 286, 386, 486, Pentium, PentiumII, PentiumIII, Pentium4, Core2, Core i7, …

## Slide 21: Recall: CPU Performance Equation
Latency = seconds / program =
  (insns / program) * (cycles / insn) * (seconds / cycle)
  Insns / program: insn count
    Impacted by program, compiler, ISA
  Cycles / insn: CPI
    Impacted by program, compiler, ISA, micro-arch
  Seconds / cycle: clock period (Hz)
    Impacted by micro-arch, technology
For low latency (better performance) minimize all three
  Difficult: often pull against one another
  Example we have seen: RISC vs. CISC ISAs
    RISC: low CPI/clock period, high insn count
    CISC: low insn count, high CPI/clock period
Notes: Have leaned in CMPE 110
Can be calculated in this way

## Slide 22: Performance, Performance, Performance
How long does it take for a program to execute?
  Three factors
1. How many insn must execute to complete program?
  Instructions per program during execution
  “Dynamic insn count” (not number of “static” insns in program)
2. How quickly does the processor “cycle”?
  Clock frequency (cycles per second) 1 gigahertz (Ghz)
  or expressed as reciprocal, Clock period nanosecond (ns)
  Worst-case delay through circuit for a particular design
3. How many cycles does each instruction take to execute?
  Cycles per Instruction (CPI) or reciprocal, Insn per Cycle (IPC)
  Execution time = (instructions/program) * (seconds/cycle) * (cycles/instruction)

## Slide 23: Maximizing Performance
Instructions per program:
  Determined by program, compiler, instruction set architecture (ISA)
Cycles per instruction: “CPI”
  Typical range today: 2 to 0.5
  Determined by program, compiler, ISA, micro-architecture
Seconds per cycle: “clock period”
  Typical range today: 2ns to 0.25ns
  Reciprocal is frequency: 0.5 Ghz to 4 Ghz (1 Hz = 1 cycle per sec)
  Determined by micro-architecture, technology parameters
For minimum execution time, minimize each term
  Difficult: often pull against one another
  (1 billion instructions) * (1ns per cycle) * (1 cycle per insn) = 1 second
  Execution time = (instructions/program) * (seconds/cycle) * (cycles/instruction)

## Slide 24: Example: Instruction Granularity
CISC (Complex Instruction Set Computing) ISAs
  Big heavyweight instructions (lots of work per instruction), complex
  Low “insns/program”
  Higher “cycles/insn” and “seconds/cycle”
    We have the technology to get around this problem
    More work, more time
RISC (Reduced Instruction Set Computer) ISAs
  Minimalist approach to an ISA: simple insns only
  Low “cycles/insn” and “seconds/cycle”
  Higher “insn/program”, but hopefully not as much
    Rely on compiler optimizations
  Execution time = (instructions/program) * (seconds/cycle) * (cycles/instruction)

## Slide 25: CISC vs. RISC
CISC (M68000):
Add (A3)+, 100(A2)
Add the content of memory location pointed to by A3 to the component of an array starting at memory address 100. The index number of the component is in A2. The content of A3 is then automatically incremented by 1.
RISC (MIPS):
Lw $t0, 0($s3)
Lw $t1, 100 ($s2)
Add $t2, $t0, $t1
Sw $t2, 100($s3)
Addi $s3, $s3, 1
    Both execute the same instruction

## Slide 26: The Debate
RISC argument
  CISC is fundamentally handicapped
  For a given technology, RISC implementation will be better (faster)
    Current technology enables single-chip RISC
    When it enables single-chip CISC, RISC will be pipelined
    When it enables pipelined CISC, RISC will have caches
    When it enables CISC with caches, RISC will have next thing...
CISC rebuttal
  CISC flaws not fundamental, can be fixed with more transistors
  Technology advancement will narrow the RISC/CISC gap (true)
    Good pipeline: RISC = 100K transistors, CISC = 300K
    By 1995: 2M+ transistors had evened playing field
  Software costs dominate, compatibility is paramount
Notes: What was Intel’s trick?

## Slide 27: Compiler Optimizations
Primarily goal: reduce instruction count
  Eliminate redundant computation, keep more things in registers
    Registers are faster, fewer loads/stores
    An ISA can make this difficult by having too few registers
But also…
  Reduce branches and jumps
  Reduce cache misses
  Reduce dependences between nearby insns
  An ISA can make this difficult by having implicit dependences
How effective are these?
  Can give 4X performance over unoptimized code
  Collective wisdom of 40 years (“Proebsting’s Law”): 4% per year
  Funny but … shouldn’t leave 4X performance on the table
Notes: Todd Proebsting: compiler optimization advances double computing power every 18 years.

## Slide 28: What Makes a Good ISA?
Programmability
  Easy to express programs efficiently?
Performance/Implementability
  Easy to design high-performance implementations?
  Easy to design low-power implementations?
  Easy to design low-cost implementations?
Compatibility
  Easy to maintain as languages, programs, and technology evolve?
  x86 (IA32) generations: 8086, 286, 386, 486, Pentium, PentiumII, PentiumIII, Pentium4, Core2, Core i7, …

## Slide 29: Compatibility
In many domains, ISA must remain compatible
  IBM’s 360/370 (the first “ISA family”)
  Another example: Intel’s x86 and Microsoft Windows
    x86 one of the worst designed ISAs EVER, but it survives
Backward compatibility
  New processors supporting old programs
    Hard to drop features
    Update software/OS to emulate dropped features (slow)
Forward (upward) compatibility
  Old processors supporting new programs
    Include a “CPU ID” so the software can test for features
    Add ISA hints by overloading no-ops (example: x86’s PAUSE)
    New firmware/software on old processors to emulate new insn
Notes: X86 is CISC

## Slide 30: Translation and Virtual ISAs
New compatibility interface: ISA + translation software
  Binary-translation (static): transform static image, run native
  Emulation (dynamic binary-translation): unmodified image, interpret each dynamic insn
    Typically optimized with just-in-time (JIT) compilation
  Examples: DEC FX!32 (x86 on Alpha), Rosetta (PowerPC on x86)
  Performance overheads reasonable (many advances over the years)
Virtual ISAs: designed for translation, not direct execution
  Target for high-level compiler (one per language)
  Source for low-level translator (one per ISA)
  Goals: Portability (abstract hardware nastiness), flexibility over time
  Examples: Java Bytecodes, C# CLR (Common Language Runtime), NVIDIA’s “PTX”
Notes: diff wrt virtualization software like VMWare, Virtual PC, Parallels, Xen, etc.

## Slide 31: Ultimate Compatibility Trick
Support old ISA by…
  …having a simple processor for that ISA somewhere in the system
  How did PlayStation2 support PlayStation1 games?
    Used PlayStation processor for I/O chip & emulation

## Slide 32: What we learned
What is ISA?
Program execution model:
  Compilation
  Assembly & machine language
Instruction execution model
  Registers, memory, PC
  Instruction execution
ISA design goals
  Programmability
  Performance/implementability
  Compatibility
CPU
Mem
I/O
System software
App
App
App
Fetch
Decode
Read Inputs
Execute
Write Output
Next Insn

## Slide 33: Aspects of ISAs

## Slide 34: Length and Format
Length
  Fixed length
    Most common is 32 bits
    Simple implementation (next PC often just PC+4)
    Code density: 32 bits to increment a register by 1
  Variable length
    Code density
      x86 averages 3 bytes (ranges from 1 to 16)
    Complex fetch (where does next instruction begin?)
  Compromise: two lengths
    E.g., MIPS16 or ARM’s Thumb (16 bits)
Encoding
  A few simple encodings simplify decoder
  Machine code (1s and 0s) <-> assembly
Fetch[PC]
Decode
Read Inputs
Execute
Write Output
Next PC
Notes: Machine code mapped to assemply

## Slide 35: Example Instruction Encodings
MIPS
  Fixed length
  32-bits, 3 formats, simple encoding
x86
  Variable length encoding (1 to 15 bytes)
Op(6)
Rs(5)
Rt(5)
Rd(5)
Sh(5)
Func(6)
R-type
Op(6)
Rs(5)
Rt(5)
Immed(16)
I-type
Op(6)
Target(26)
J-type
Op
OpExt*
ModRM*
SIB*
Disp*(1-4)
Imm*(1-4)
Prefix*(1-4)
add R1,R2,R3

## Slide 36: Where Does Data Live?
Fetch
Decode
Read Inputs
Execute
Write Output
Next Insn

## Slide 37: Where Does Data Live?
Registers (e.g., R0, R1, F0)
  “short term memory”
  Faster than memory, quite handy
  Named directly in instructions
Memory (e.g., (R3), #20(R5) )
  “longer term memory”
  Accessed via “addressing modes”
    Address to read or write calculated by instruction
“Immediates” (e.g., #36, #7)
  Values spelled out as bits in instructions
  Input only
Fetch
Decode
Read Inputs
Execute
Write Output
Next Insn
ADD R1,R2,R3
ADD R1,R2,(R3)

## Slide 38: Memory Addressing
…
0x0003
0x0004
0001 0111
1001 0101
0101 0110
Addresses
Data
0x0001
0x0002
Notes: displ:object, idx-base:array, mem-ind:**, scaled:array-of-structs, pc-rel:constant in insn memory

## Slide 39: Memory Addressing
Addressing mode: way of specifying address
Examples
  Displacement: address = [R2+immed], e.g., #20(R2)
  Index-base: address = [R2+R3]
  Memory-indirect: address =[mem[R2]]
  Auto-increment: address=[R2], R2= R2+1
  Auto-indexing: address =[R2+immed], R2=R2+immed
  Scaled: address =[R2+R3*immed1+immed2]
  PC-relative: address =[PC+imm]
Notes: displ:object, idx-base:array, mem-ind:**, scaled:array-of-structs, pc-rel:constant in insn memory

## Slide 40: Control Transfers
Default next-PC = PC + sizeof(current insn)
  Branches and jumps can change that
Computing targets: where to jump to
  For all branches and jumps
  PC-relative: e.g., bne R3, R6, L3 for branches and jumps with function
  Absolute: e.g., J L3 for function calls
  Register indirect: e.g., JR R5 for returns, switches & dynamic calls
Testing conditions: whether to jump or not
  Use registers & separate branch insns (MIPS)
    e.g., bnez R2,target
Fetch
Decode
Read Inputs
Execute
Write Output
Next Insn
  J L3

## Slide 41: Summary: ISA
What is ISA?
Execution model:
  Compilation
  Assembly & machine language
Instruction execution model
  Registers, memory, PC
  Instruction execution
ISA design goals
  Programmability
  Performance/implementability
  Compatibility
Aspects of ISAs
CPU
Mem
I/O
System software
App
App
App
Fetch
Decode
Read Inputs
Execute
Write Output
Next Insn