## Slide 1: CMPE 110: Computer Architecture
Week 2
ISA II
[Adapted in part from Jose Renau, Mary Jane Irwin, Joe Devietti, Onur Mutlu, and others]
Jishen Zhao (http://users.soe.ucsc.edu/~jzhao/)

## Slide 2: Reminder
Homework 1 will be posted on course Google site by today 4pm
  Performance and ISA
  Due by midnight Jan. 24

## Slide 3: Review: ISA Overview
What is an ISA?
  An ISA includes a specification of the set of opcodes and the native commands implemented by a particular processor. <Wikipedia>
Program execution model
  High-level programming language (C/C++/Java/C#/…)
  Assembly language
    Human-readable representation
  Machine language
    1s and 0s (often displayed in “hex”)
Instruction execution model
CPU
Mem
I/O
System software
App
App
App
Fetch
Decode
Read Inputs
Execute
Write Output
Next Insn

## Slide 4: Review: An ADD Documentation
Notes: Too small, read out

## Slide 5: Review: ISA vs. Performance
Latency = seconds / program =
  (insns / program) * (cycles / insn) * (seconds / cycle)
  Insns / program: insn count
    Impacted by program, compiler, ISA
  Cycles / insn: CPI
    Impacted by program, compiler, ISA, micro-arch
  Seconds / cycle: clock period (Hz)
    Impacted by micro-arch, technology
How does ISA affect insn count and CPI?
  Example: CISC vs. RISC

## Slide 6: CISC vs. RISC
CISC (Complex Instruction Set Computing) ISAs
  Examples: Intel/AMD x86, IBM System/360, Intel 8051
  Big heavyweight instructions (lots of work per instruction)
  Low “insns/program”
  Higher “cycles/insn” and “seconds/cycle”
RISC (Reduced Instruction Set Computer) ISAs
  Examples: MIPS, ARM, Alpha
  Simple instructions only: minimalist approach to an ISA
  + Low “cycles/insn” and “seconds/cycle”
  Higher “insn/program”, but hopefully not as much

## Slide 7: Today: ISA / Pipelining
ISA design goals
  Programmability
  Performance/implementability
  Compatibility
Aspects of ISAs
Pipelining
Notes: Overview of today’s class:
Metrics, how measure CPU performance,

## Slide 8: ISA Design Goals

## Slide 9: What Makes a Good ISA?
Programmability
  Easy to express programs efficiently?
Performance/Implementability
  Easy to design high-performance implementations?
  Easy to design low-power implementations?
  Easy to design low-cost implementations?
Compatibility
  Easy to maintain as languages, programs, and technology evolve?
  x86 (IA32) generations: 8086, 286, 386, 486, Pentium, PentiumII, PentiumIII, Pentium4, Core2, Core i7, …

## Slide 10: Compatibility
In many domains, ISA must remain compatible
  IBM’s 360/370 (the first “ISA family”)
  Another example: Intel’s x86 and Microsoft Windows
    x86 one of the worst designed ISAs EVER, but it survives
Backward compatibility
  New processors supporting old programs
    Hard to drop features
    Update software/OS to emulate dropped features (slow)
Forward (upward) compatibility
  Old processors supporting new programs
    Include a “CPU ID” so the software can test for features
    Add ISA hints by overloading no-ops (example: x86’s PAUSE)
    New firmware/software on old processors to emulate new insn

## Slide 11: Translation and Virtual ISAs
New compatibility interface: ISA + translation software
  Binary-translation (static): transform static image, run native
  Emulation (dynamic binary-translation): unmodified image, interpret each dynamic insn
    Typically optimized with just-in-time (JIT) compilation
  Examples: DEC FX!32 (x86 on Alpha), Rosetta (PowerPC on x86)
  Performance overheads reasonable (many advances over the years)
Virtual ISAs: designed for translation, not direct execution
  Target for high-level compiler (one per language)
  Source for low-level translator (one per ISA)
  Goals: Portability (abstract hardware nastiness), flexibility over time
  Examples: Java Bytecodes, C# CLR (Common Language Runtime), NVIDIA’s “PTX”
Notes: diff wrt virtualization software like VMWare, Virtual PC, Parallels, Xen, etc.
Rosetta is a dynamic binary translator for Mac OS X that allows many PowerPC applications to run on certain Intel-based Macintosh computers without modification. Apple released Rosetta in 2006 when it changed the instruction set architecture of the Macintosh platform from the PowerPC to the Intel processor.
Virtual ISA: An instruction set that can be compiled to, but requires additional transformations before it can be executed by hardware. The idea is that you can do most of the compiler optimizations on the virtual ISA and then target many different processors by doing simple instruction to instruction translations.

## Slide 12: Ultimate Compatibility Trick
Support old ISA by…
  …having a simple processor for that ISA somewhere in the system
  How did PlayStation2 support PlayStation1 games?
    Used PlayStation processor for I/O chip & emulation

## Slide 13: What we learned
What is ISA?
Execution model:
  Compilation
  Assembly & machine language
Instruction execution model
  Registers, memory, PC
  Instruction execution
ISA design goals
  Programmability
  Performance/implementability
  Compatibility
CPU
Mem
I/O
System software
App
App
App
Fetch
Decode
Read Inputs
Execute
Write Output
Next Insn

## Slide 14: Aspects of ISAs

## Slide 15: Aspects of ISAs
Instruction length and format
  Instruction encoding
Where does data live?
  Addressing modes
Control transfers
  How to find the next instruction
  Branch
  Jump
Fetch
Decode
Read Inputs
Execute
Write Output
Next Insn

## Slide 16: Length and Format
Length
  Fixed length
    Most common is 32 bits
    Simple implementation (next PC often just PC+4)
    Code density: 32 bits to increment a register by 1
  Variable length
    Code density
      x86 averages 3 bytes (ranges from 1 to 16)
    Complex fetch (where does next instruction begin?)
  Compromise: two lengths
    E.g., MIPS16 or ARM’s Thumb (16 bits)
Encoding
  A few simple encodings simplify decoder
  Machine code (1s and 0s) <-> assembly
Fetch[PC]
Decode
Read Inputs
Execute
Write Output
Next PC
Notes: Machine code mapped to assemply

## Slide 17: Example Instruction Encodings
MIPS
  Fixed length
  32-bits, 3 formats, simple encoding
x86
  Variable length encoding (1 to 15 bytes)
Op(6)
Rs(5)
Rt(5)
Rd(5)
Sh(5)
Func(6)
R-type
Op(6)
Rs(5)
Rt(5)
Immed(16)
I-type
Op(6)
Target(26)
J-type
Op
OpExt*
ModRM*
SIB*
Disp*(1-4)
Imm*(1-4)
Prefix*(1-4)
add R1,R2,R3

## Slide 18: Where Does Data Live?
Fetch
Decode
Read Inputs
Execute
Write Output
Next Insn

## Slide 19: Where Does Data Live?
Registers (e.g., R0, R1, F0)
  “short term memory”
  Faster than memory, quite handy
  Named directly in instructions
  F = Floating point registers (Special registers)
Memory (e.g., (R3), #20(R5) )
  “longer term memory”
  Accessed via “addressing modes”
    Address to read or write calculated by instruction
“Immediates” (e.g., #36, #7)
  Values spelled out as bits in instructions
  Input only
Fetch
Decode
Read Inputs
Execute
Write Output
Next Insn
ADD R1,R2,R3
ADD R1,R2,(R3)

## Slide 20: Memory Addressing
…
0x0003
0x0004
0001 0111
1001 0101
0101 0110
Addresses
Data
0x0001
0x0002
Notes: displ:object, idx-base:array, mem-ind:**, scaled:array-of-structs, pc-rel:constant in insn memory

## Slide 21: Memory Addressing
Addressing mode: way of specifying address
Examples
  Displacement: address = [R2+immed], e.g., #20(R2)
  Index-base: address = [R2+R3]
  Memory-indirect: address =[mem[R2]]
  Auto-increment: address=[R2], R2= R2+1
  Auto-indexing: address =[R2+immed], R2=R2+immed
  Scaled: address =[R2+R3*immed1+immed2]
  PC-relative: address =[PC+imm]
Notes: displ:object, idx-base:array, mem-ind:**, scaled:array-of-structs, pc-rel:constant in insn memory

## Slide 22: Control Transfers
Default next-PC = PC + sizeof(current insn)
  Branches and jumps can change that
Computing targets: where to jump to
  For all branches and jumps
  PC-relative: e.g., J offset for branches and jumps with function
  Absolute: e.g., J L3 for function calls
  Register indirect: e.g., JR R5 for returns, switches & dynamic calls
Testing conditions: whether to jump or not
  Use registers & separate branch insns (MIPS)
    e.g., bnez R2,target
Fetch
Decode
Read Inputs
Execute
Write Output
Next Insn
  J L3
-4

## Slide 23: Summary: ISA
What is ISA?
Execution model:
  Compilation
  Assembly & machine language
Instruction execution model
  Registers, memory, PC
  Instruction execution
ISA design goals
  Programmability
  Performance/implementability
  Compatibility
Aspects of ISAs
CPU
Mem
I/O
System software
App
App
App
Fetch
Decode
Read Inputs
Execute
Write Output
Next Insn